Produksi Renium–188(188Re) dari Generator 188W/188Re Menggunakan Eluen Asam

Askorbat (Duyeh Setiawan dan Muljadji Agma)

PRODUKSI RENIUM – 188 (188Re) DARI GENERATOR 188W/188Re

MENGGUNAKAN ELUEN ASAM ASKORBAT

Duyeh Setiawan 1 dan Muljadji Agma 2

1 Puslitbang Teknik Nuklir – Batan Bandung

2 Jurusan Kimia FMIPA – Unpad Bandung

ABSTRAK

Telah dilakukan penelitian dalam upaya meminimalkan pengurangan hasil produksi radionuklida 188Re dari generator 188W/188Re cara penyimpanan basah. Bahan dasar kolom sebagai matriks generator 188W/188Re yang digunakan alumina yang mengikat radionuklida 188W untuk menghasilkan radionuklida 188Re melalui proses peluruhan. Pemisahan radionuklida 188Re dalam generator 188W/188Re dilakukan dengan cara elusi menggunakan eluen dari campuran larutan NaCl 0,9 % yang mengandung asam askorbat (Acidum ascorbicum). Penambahan asam askorbat dalam eluen memberikan hasil elusi produksi radionuklida 188Re yang dapat dipertahankan lebih besar dari 70 %. Sedangkan elusi tanpa penambahan asam askorbat diperoleh hasil radionuklida 188Re berkurang menjadi dibawah 50 %. Penambahan asam askorbat kedalam eluen dengan konsentrasi rendah sejumlah 0,025 % merupakan suatu cara anternatif yang efektif untuk mempertahankan kualitas hasil elusi radionuklida 188Re dari generator 188W/188Re setelah penyimpanan basah selama 120 jam. Kemurnian radionuklida 188Re menunjukkan tidak terlihat adanya pengotor dari radionuklida lain terutama radionuklida 188W yang merupakan radionuklida induk. Hasil kromatogram menunjukkan migrasi 188Re memberikan harga Rf = 0,75 - 0,8 dengan kemurnian radiokimia lebih besar 98 %.

Kata kunci :produksi, radioisotop, generator, renium-188, asam askorbat.

RHENIUM – 188 ( 188Re) PRODUCTION FROM 188W/188Re GENERATORS

USING ASCORBIC ACID ELUENT

ABSTRACT

In an attempt to minimize the reduced yields of radionuclide 188Re production with wet storage of 188W/188Re  generators has been done. The column bed material as matrix of 188W/188Re generators used were alumina binding to radionuclide 188W to produce radionuclide 188Re by decay process. The radionuclide 188Re separation in the 188W/188Re generators was done with the use 1 Staf pengajar LB Jurusan Kimia FMIPA – Unpad Bandung of eluent mixture of NaCl 0.9 % solution containing ascorbic acid (Acidum ascorbicum). In countrast, addition of ascorbic acid in the eluen was found radionuclide 188Re production can be maintaining of elution yield more than 70 %. Whereas non addition of ascorbic acid found radionuclide 188Re decreased under 50 %. The addition of ascorbic acid at concentration as low as 0.025 % in the eluent was found to be effective alternative method of quality maintaining ofradionuclide 188Re elution of 188W/188Re generators with wet storage method after 120 hours. The radionuclide 188Re show that there is no appearance of radionuclide pollutant especially radionuclide 188W as parent radionuclide. The result of chromatogram shows that the migration of 188Re give a Rf = 0.75 - 0,8 with a radiochemical purity more than 98  %.

Key words : production, radioisotope, generators, rhenium-188, ascorbic acid.